# XRMC (X-ray Monte Carlo) version 6.4.1
# TUTORIAL

Bruno Golosio, Tom Schoonjans, Antonio Brunetti, Giovanni Luca Masala, Piernicola Oliva
Università degli Studi di Sassari

Copyright & Disclaimer
© 2013 Bruno Golosio. This tutorial is part of the XRMC software package. XRMC is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version. This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details. You should have received a copy of the GNU General Public License along with this program. If not, see <http://www.gnu.org/licenses/>.

## Installation
### Requirements
The following requirements exist for building XRMC:
ANSI-C Compiler and Build System
Make sure you have an ANSI-C compiler installed. The GNU C compiler (GCC) from the Free Software Foundation (FSF) is recommended. If you don't have GCC then at least make sure your vendor's compiler is ANSI compliant. In addition, your PATH must contain basic build tools such as make.
xraylib (version >= 2.15.0)
To compile XRMC you need the xraylib shared library version >= 2.15.0 .
xraylib is a library of x-ray interaction parameters, freely available for several platforms at the following URL:

 http://github.com/tschoonj/xraylib

Note that only the xraylib shared library is needed for XRMC installation. The command line tool and the bindings are not necessary, although they can be valuable tools for researchers working with x-rays.
This version of XRMC was tested with xraylib v2.16.0
### Extracting the source
Extract the source using any program able to extract/uncompress tar.gz archives.
For instance, in Linux, Unix and Unix-like systems you can extract the source using the gzip utility, by typing the command:

gunzip -xvzf xrmc-x.x.x.tar.gz

where x.x.x refers to the version of the program that you are installing. This will create a new directory xrmc-x.x.x under the current directory containing the source code for the distribution.
### Building and installing the program
There are two main methods of installing XRMC from source: system wide installation and personal installation. The former requires root privileges on most systems. Both ways are described below.

System wide installation
After unpacking the distribution, go to the directory "xrmc-x.x.x" (where x.x.x refers to the version of the program that you are installing) and type the command:

./configure

You can then build the program by typing,

make

To verify that the build went ok, use,

make check

The installation can be performed with the command

make install

The default installation directory prefix is /usr/local.
The installation directory can be changed with the --prefix option to configure. Consult the "Further information" section below for instructions on installing the library in another location or changing other default compilation options.
On some systems you might need to update the ldconfig cache by doing:

ldconfig

Try running XRMC:

xrmc

Personal installation
After unpacking the distribution, go to the directory "xrmc-x.x.x" (where x.x.x refers to the version of the program that you are installing) and type the command:

./configure --prefix=DIRNAME

where DIRNAME is the name of the directory where you want to install the binary executable and the libraries.
You can then build the program by typing,

make

To verify that the build went ok, use,

make check

The installation can be performed with the command

make install

This command will install the executable in the subdirectory bin/ of the installation directory, and the libraries in the subdirectory lib/
You should add the subdirectories bin/ and /lib to the PATH and to the LD_LIBRARY_PATH environmental variables, respectively.
For instance, if you use the bash shell you can add the following lines to the file .bashrc (or bashrc_private if you use it) in your home directory:

export PATH=${PATH}:DIRNAME/bin:
export LD_LIBRARY_PATH=${LD_LIBRARY_PATH}:DIRNAME/lib:

If you use the tcsh shell you can add the following lines to the file .cshrc
(or cshrc_private if you use it) in your home directory:
setenv PATH ${PATH}:DIRNAME/bin:
setenv LD_LIBRARY_PATH ${LD_LIBRARY_PATH}:DIRNAME/lib:

Try running XRMC:

xrmc
### Platforms known to compile and run XRMC
  Linux (32-bit/64-bit)
  Mac OS X (32-bit/64-bit)
  Windows (native and Cygwin)

In principle, it should be possible to compile and run XRMC in any platform that supports the xraylib library. See the section "Platforms known to compile and run xraylib" in the INSTALL documentation file of xraylib for further information.
## Support
Sorry, we don't give any kind of support to XRMC users besides this tutorial, mainly because we lack human resources for doing it. You can use the program freely if you find it useful, however please don't write us emails asking for help with your simulations, or asking for explanations if they do not give the results that you expect.
## Bugs
For sure there are bugs in XRMC. In every new version of the code we try fix bugs from previous versions. If you find a bug, your feedback will be greatly appreciated. However, bugs should be reported in a proper way. If you believe that there is a bug in the program, please try to insulate it, reducing your setup to the minimum one that presents such problem, and send your bug report together with the configuration files to golosio@uniss.it .
## Getting started
This section contains some basic advises for new XRMC users.
- It can be useful to start working with existing examples, which are described in section 6. You can choose the example that is more similar to the experimental conditions that you want to simulate. First, run the example as it is and display the results of the simulation. Then you can try to modify the example to make it closer to the setup that you want to simulate. It is better that you modify one device file at a time, so that in case something does not work as you want you know where is the problem.
- The current version of XRMC does not include tools to visualize the experimental setup. However, you can use the program itself to visualize radiographic projections of the sample. Even if you want to run a simulation with a single element detector (for instance if you are simulating a spectroscopy measurement) it can be useful to define also a second source and an array detector, as those used in the imaging examples, loaded by a second input file, used only for visualization purpose. In this way you can check if the sample geometry looks correct.
- If the sample geometry does not look as you expect, try to visualize only one three-dimensional object at a time. You can do this easily by commenting all the lines corresponding to the other objects in the geom3d file, as described in section 5.8.
- When defining the geometric description of the sample, pay particular attention to XRMC limitations in three-dimensional objects definition, as outlined in section 5.8.
- At the beginning, run your simulations with a very small number of events, just to check that everything is working fine. Increase the number of events gradually to check that the output is reasonable before running very long simulations.
## Using the program
Before running XRMC, you must prepare the input files that describe the experimental setup that you want to simulate. Those files include a main input file, a parameter file and some device files. The term device refers to a C++ object that is created to be used by the simulation and whose parameters are loaded from the corresponding file. It is not necessarily a physical device. For instance, the phase (material) array and the sample are considered to be devices. Each device file consists of a header that specifies the type and name of the device, a list of commands or variable names, and finally the “End” command. The order of commands/variable names is generally not important, unless they are part of the same group (for instance, the atomic number and weight percent of the elements in a material), as described in the following paragraphs. Each command/variable name can be followed by one or more arguments (real values, integer values or strings, depending on the command). Command/variable names need not to be in the same line. Comments can be inserted in all input files by preceding them by any of the following characters: ';', '!' or '#'. XRMC is case sensitive. Most commands and variable names in the input files follow the CamelCase convention, i.e. the first letter of each concatenated word is capitalized. The following paragraphs describe the commands that can be used in all device files used by the program. Although all variables have a default value, and therefore most commands are not mandatory, it is strongly recommended to explicitly assign a value to all variables in the input files.
### The main input file
The main input file specifies the commands for loading all device files, the command for running the simulation and the command for saving the output in a file.
A device is created, and its parameters are loaded from a file, through the command:
Load filename
where filename is the name of the device file.
The typical setup for x-ray imaging/spectroscopy simulations include the following devices:
- a source (source device);
- a spectrum (spectrum device);
- a detector (detectorarray device);
- a sample (sample device);
- a phase (material) composition array (composition device);
- a quadric array (quadricarray device);
- a three-dimensional object geometric description (geom3d device).
The associated input files are described in the following sections.
The order of the “Load” commands is not relevant.
After such commands, the simulation can be started by the command
Run devicename
where devicename is the name of the device that controls the acquisition of the simulation results, i.e. in x-ray imaging/spectroscopy simulations the name of the detectorarray device, as specified in the header of the corresponding file.
Finally, the result of the simulation is saved by the command
Save devicename dataname filename
where devicename has the same meaning as described for the previous command, dataname is a name associated to the data that should be saved, and filename is the name of the file used to save the results. The allowed entries for dataname depend on the device; for the detectorarray device the only allowed entry for dataname is Image.
### The device files
Every file for defining a new device has the following structure:

Newdevice device-type device-name	; New device file header
command/variable-name arguments
…
End

It is also possible to change the setup for an already-defined device, using the command

Device device-name

in place of the Newdevice command. The following sections describe the commands for the devices available in the current version of the program.
### The spectrum file
The source spectrum is modeled as the sum of two components: a set of discrete lines and a continuous component. The radiation can be unpolarized, partially polarized or totally polarized. The lines can have a Gaussian or a Dirac d distribution (the latter one being simply a particular case of Gaussian distribution with s = 0). Each line is specified by its mean energy El, by its intensity Il and by sl.
In case of (partially or totally) polarized radiation, the intensity of the two components polarized along the local x and y directions are specified separately for each line.
The continuous component is defined by N samples at arbitrary energies E1, …., EN, by specifying for each sample the corresponding height of the spectral distribution I1, …., IN. The height of the distribution in the interval between two consecutive energies of the sample Ei, Ei+1 is approximated by a linear function of E that goes from Ii to Ii+1, therefore the spectrum in each interval between two consecutive samples has a trapezoidal shape. The area of the trapezium (Ei+1 – Ei)·(Ii + Ii+1)/2 represents the intensity of the interval. In case of (partially or totally) polarized radiation, the height of the x and y components are specified separately for each sample of the continuous component.
There are two possible ways of extracting the initial energy of x-ray photons produced by the source:
1. extract random energies on the whole spectrum: the photon initial energy is extracted using the whole spectrum itself as a probability distribution;
2. loop on all lines and on all intervals of the spectrum: a loop is made on all lines and on all intervals of the spectrum; the initial energy of the photon is extracted according to the probability distribution limited to the single line or to the single interval; the event is assigned a weight proportional to the line/interval intensity.
The first is the traditional Monte Carlo approach. Lines or regions of the spectrum with lower intensity
are less represented in the generated statistic, no matter how important is the contribution that they give to the detected signal. There can be some drawback in this approach. For instance, if the spectrum has a relative low intensity at higher energies and if the sample is a strongly absorbing object, the statistic of events with higher energies will be low even though they give the most important contribution to the detected signal.
The second approach is closer to deterministic integration methods and should normally be preferred to the first one. All lines and all interval are equally represented in the generated statistic, and their relative probability is corrected by using the method of weighting the event.
If the second method is chosen, than for each interval of the continuous component there are two possible ways of extracting the photon energy:
1. extract the energy randomly according to the probability distribution inside the interval itself (which is modeled by a linear function, as discussed previously);
2. force the photon energy to be equal to the central energy of the interval.
The second method is the pure deterministic approach, and normally it should not be used.
The program offers the opportunity to resample the continuous component after its definition. In this case, the user must specify the starting energy, the energy step and the number of points used for the resampling. The intensities Ii are then recalculated for the new values of Ei. Normally this option will not be used, however it may be useful for variance reduction if the space between sampling energies in the continuous component definition is too large and a finer separation is desired or, in the opposite case, if the energy step in the initial definition of the spectrum is unnecessarily too small.

spectrum device file header:

Newdevice spectrum	; Device type
name (string)	; Device name

Commands:

PolarizedFlag val
specifies if the beam is polarized:
val = 0: unpolarized beam;
val = 1: polarized beam;

LoopFlag val
energy extraction method:
val = 0: extract random energies on the whole spectrum;
val = 1: loop on all lines and sampling points;

ContinuousPhotonNum val
val (integer): multiplicity of events for each interval in spectrum;

LinePhotonNum val
val (integer): multiplicity of events for each line in spectrum;

RandomEneFlag val
enable/disable random energy in each interval of the continuous spectrum;
val = 0: random energy disabled;
val = 1: random energy enabled (recommended);

Lines
specifies the discrete energy lines of the spectrum;
energies and s are expressed in keV:
Nl (integer): Number of lines in the spectrum
El sl Il (real values): energy, width (rms) and intensity of the 1st line
    …..
ENl sNl INl (real values): energy, width (rms) and intensity of the Nth line
 for polarized beam, or
El sl Ix1 Iy1 (real values):
energy, width (rms) and intensities of the two polarization components of the 1st line
    …..
ENl sNl IxNl IyNl (real values):
energy, width (rms) and intensities of the two polarization components of the Nth line

ContinuousSpectrumFile
continuous component of the spectrum;
NI (integer): Number sampling points in the continuous spectrum
filename : name of the file containing the continuous spectrum;
in the case of unpolarized beam, the file has the following format:
El Il (real values): energy and intensity of the 1st sampling point
    …..
ENI INI (real values): energy and intensity of the Nth sampling point;
while for polarized beam it has the following format:
El Ix1 Iy1 (real values):
energy and intensities of the two polarization components of the 1st sampling point
    …..
ENI IxNI IyNI (real values):
energy and intensityies of the two polarization components of the Nth sampling point;

ContinuousSpectrum
same as ContinuousSpectrumFile, but the spectrum is loaded inline rather than from an external file. Clearly, the filename parameter is not used in this case

Resample val
val = 0: do not resample continuous spectrum;
val = 1: resample continuous component of the spectrum;
If val = 1, the following arguments must also be provided:
NR (integer): number of resampling points;
Emin (real): minimum resampling energy (keV);
Emax (real): maximum resampling energy (keV);

End
End of file.

The total number of generated events is given by the product of the multiplicities in the spectrum, in the interactions with the sample and in the detector pixels.

jd
js

id

kd
rs
rd
ks

Sample
Source

photon

is

Detector

Figure 1. The standard experimental setup simulated by XRMC consists of a x-ray source, a sample and a detector (two-dimensional array or single element). A local coordinate system is attached to the source and to the detector. rs and rd are the position vector of the source and of the detector geometric center, respectively. is, js and ks are the directions of the source local x, y, and z axis, respectively. id, jd and kd are the directions of the detector local x, y, and z axis, respectively. The detector local z axis is perpendicular to the detector surface, while the local x and y axes are parallel to the detector rows and columns, respectively.

### The source file
The current version of the code assumes that the x-ray beam is produced by a point source or by an extended source with a three-dimensional Gaussian distribution. A local coordinate system is associated to the source, specified by the vector position of the origin rs and by the orthonormal unit vectors is, js and ks (see Fig. 1), which are the directions of the local x, y, and z axis, respectively. The local z axis represents the main source direction, while the local x and y axes are used to define the beam polarization and angular aperture. Let qs and fs be the polar and azimuthal angle, respectively, relative to the source coordinate system. The user can specify the angular apertures qx and qy in the x and in the y direction, respectively. In general, the angular aperture of the source is elliptical and it is defined by the inequality:

q2 ≤ qx2cos2fs + qy2sin2fs

The source intensity distribution is assumed to be uniform within the solid angle limited by this angular aperture.

source device file header:

Newdevice source	; Device type
name (string)	; Device name

Commands:

SpectrumName name
name (string): spectrum input device name;

X val1 val2 val3
val1, val2, val3 (real values) source x, y, z coordinates

uk val1 val2 val3
source orientation: ks components (local z axis direction, i.e. main source direction);
val1 val2 val3 (real values): ksx, ksy, ksz

ui val1 val2 val3
source orientation: is components (local x axis direction);
val1 val2 val3 (real values): isx, isy, isz

Divergence val1 val2
beam divergence:
val1 val2 (real values): qx , qy

Size val1 val2 val3
Source size; the source is modeled as a three-dimensional Gaussian distribution:
val1 val2 val3 (real values) sx, sy, sz ;

Rotate val1 val2 val3 val4 val5 val6 val7
rotation of the source around the axis passing through x0 and with direction u :
val1 val2 val3 (real values): x0, y0, z0 ;
val4 val5 val6 (real values): ux, uy, uz ;
val7 (real) rotation angle q (degrees);

End
End of file.

If is is not perpendicular to ks , then the program replace it by a vector on the same common plane, but perpendicular to ks. If ks or is are not unit vectors then they are normalized by the program. The vector js is computed by the program, so that is , js , ks are orthonormal unit vectors.
### The detector file
In general, the program can simulate two-dimensional array detectors with energy binning for each pixel. A single element detector can be simulated as a special case of array detector with only one pixel. The pixel shape can be defined as rectangular or elliptical. The latter possibility is particularly useful when a round, single element detector has to be simulated.
A local coordinate system is associated to the detector, specified by the vector position of its geometric center rd and by the orthonormal unit vectors id, jd and kd (see Fig. 1), which are the directions of the local x, y, and z axis, respectively. The local z axis is perpendicular to the detector surface, while the local x and y axes are parallel to the detector rows and columns, respectively.
According to a variance reduction technique used in the code, each event is forced to end with a photon that reaches a pixel of the detector (and its weight is multiplied by a proper probability factor). The intersection between the last photon trajectory and the pixel can be a random position on the pixel surface, or it can be forced to be the midpoint of the pixel. The latter method is a pure deterministic approach, and normally it should not be used.
The user has the possibility to simulate a statistical uncertainty on pixel counts based on Poisson statistic. In the traditional Monte Carlo approach the number of photons detected by each channel of each pixel is always an integer number. Using variance reduction techniques the events are weighted, therefore the estimated number of detected photons is a real number. However it is possible to round it to the closest integer number.
The weight associated to the probability that the last photon of an event reaches a detector pixel is proportional to a geometric efficiency factor egeom, which is related to the solid angle from the interaction point to the pixel surface. If the last interaction occurs at a distance from the pixel that is comparable or smaller than the pixel size, eW can become very large. In order to avoid spikes in the signal on single pixels, it is useful to set a cut on eW . By default, this cut is set to 2p.
Two acquisition modalities are possible:
1. fluence: each channel simply counts the number of photons that it detects;
2. energy fluence: each channel sums up the energy of the photons that it detects
The energy response of the detector can eventually be taken into account by using the first modality with a sufficient number of energy bins and by a proper postprocessing of the acquisition.

detectorarray device file header:

Newdevice detectorarray	; Device type
name (string)	; Device name

Commands:

SourceName name
name (string): source input device name;

NPixels val1 val2
pixel number (Nx × Ny);
val1, val2 (integer values): number of columns (Nx) and rows (Ny);

PixelSize val1 val2
pixel size (Lx × Ly , cm);
val1, val2 (real values): rectangle sides (Lx , Ly);

Shape val
pixel shape:
val = 0 : rectangular;
val = 1 : elliptical;

dOmegaLim val
cut on eW (if this entry is 0, then eW is set to the default value 2p);
val (real) eW;

X val1 val2 val3
val1, val2, val3 (real values) detector geometric center coordinates x, y, z;

uk val1 val2 val3
orientation: kd components (local z axis direction, i.e. normal to the detector surface);
val1 val2 val3 (real values): kdx, kdy, kdz

ui val1 val2 val3
detector orientation: id components (local x axis direction);
val1 val2 val3 (real values): idx, idy, idz

ExpTime val
val (real value): exposure time (seconds)

PhotonNum val
val (integer): multiplicity of simulated events per pixel;

RandomPixelFlag val
val (integer): enable random point on pixels (0/1)

PoissonFlag val
val (integer): enable Poisson statistic on pixel counts (0/1)

RoundFlag val
val (integer): round pixel counts to integer (0/1)

HeaderFlag val
val (integer): use header in output file (0/1)

AsciiFlag val
val (integer): use binary or ascii output file format (0/1)

RunningFasterFlag val
val (integer): columns(0) or rows(1) running faster in the output file

Rotate val1 val2 val3 val4 val5 val6 val7
rotation of the detector around the axis passing through x0 and with direction u :
val1 val2 val3 (real values): x0, y0, z0 ;
val4 val5 val6 (real values): ux, uy, uz ;
val7 (real) rotation angle q (degrees);

PixelType val
Pixel content type:
val (integer): 0, 1, 2 or 3;
0: fluence;
1: energy fluence;
2: fluence with energy binning;
3: energy fluence with energy binning;

Only if energy binning is used, i.e. if pixel content type is 2 or 3:

Emin val
val (real): minimum binning energy;

Emax val
val (real): maximum binning energy;

NBins val
val (integer): number of energy bins;

SaturateEmin val
val (integer): saturate energies lower than Emin (0/1)

SaturateEmax val
val (integer): saturate energies greater than Emax (0/1)

End
End of file.

If id is not perpendicular to kd , then the program replace it by a vector on the same common plane perpendicular to kd ; if kd or id are not unit vectors then they are normalized by the program; the vector jd is computed by the program, so that id , jd , kd are orthonormal unit vectors;
### The composition file
The materials that compose the sample are called phases. A composition file is used to list all the phases and to characterize them by their mass density and by their elemental composition, i.e. the atomic numbers and weight fractions of the atomic species that compose them. Each phase is assumed to be homogeneous. Phases are referred to by their user-defined names. There is a predefined phase named “Vacuum” with mass density equal to zero and no elements. This is the phase that fill the “universe”. If the user wants to simulate an experiment in a different medium (e.g. in air) he should first define it. However, only a finite region of space can be filled by a phase different from vacuum.

composition file header:

Newdevice composition	; Device type
name (string)	; Device name

Commands:

Phase name
name (string): material name; define a new material;
NElem val
val (integer):	number of atomic species Ne in the phase;
Z1 w1 (integer, real): atomic number and weight percent of 1st element;
  …..
ZNe wNe (integer, real): atomic number and weight percent of Nth element;

Rho val
val (real): mass density of the phase (g/cm3);

End
End of file.
### The quadric array file
The sample geometry is described through a set of quadrics, which are used to define the surfaces of solid objects. A quadric is a surface in the three-dimensional space defined as the locus of zeros of a quadratic polynomial. The general quadric is defined by the algebraic equation:

sum from{i,j=1} to{3} x_i Q_ij x_j + sum from{i=1} to{3} P_i x_i + R = 0 .

If we define x_0 = 1 , then the general quadric may be compactly written in vector and matrix notation as

x A x^T = 0

where x=(x_0, x_1, x_2, x_3) is a row vector, x^T is the transpose of x (a column vector) and A is a 4×4 matrix with A_ij = Q_ij for i,j=1,...,3 , A_0i = A_i0 = P_i and A_00=R .
The matrix A must be symmetric, thus A_ij=A_ji forall i,j=0,...,3 .
A quadric divides the space in two regions, one with x A x^T > 0 , the other with x A x^T < 0 .
We will call those two regions space outside the quadric (or external space) and space inside the quadric (or internal space), respectively, no matter whether the quadric is closed or not.
Whenever a unit vector normal to the quadric surface has to be defined, by default we will assume that is is oriented toward the external space. Examples of quadrics are planes, ellipsoids, cylinders.

quadricarray file header:

Newdevice quadricarray	; Device type
name (string)	; Device name

Commands:

Quadric A00 A01 A02 A03 A11 A12 A13 A22 A23 A33
Generic quadric defined by its elements' contents. Since the matrix has to be symmetric, only 10 elements are used.
- Plane x0 y0 z0 ux uy uz
  Plane containing the point (x0 , y0 , z0 ) with normal vector (ux , uy , uz).
- Ellipsoid x0 y0 z0 Rx Ry Rz
  Ellipsoid with principal axis parallel to the main axis, centered in (x0 , y0 , z0 ) and with semi-axes Rx, Ry, Rz .
- CylinderX y z Ry Rz
  Cylinder having the main axis parallel to the x axis with coordinates y, z on the yz plane, and having elliptical section with semi-axes Ry, Rz .
- CylinderY x z Rx Rz
  Cylinder having the main axis parallel to the y axis with coordinates x, z on the xz plane, and having elliptical section with semi-axes Rx, Rz .
- CylinderZ x y Rx Ry
  Cylinder with the main axis parallel to the z axis with coordinates x, y on the xy plane, and having elliptical section with semi-axes Rx, Rz .
- Translate Dx Dy Dz
  Translate the position of the last defined quadric by (Dx, Dy, Dz).
- Rotate x0 y0 z0 ux uy uz q
  Rotate the last defined quadric around the axis passing through the point (x0 , y0 , z0 ) and directed as (ux , uy , uz) by an angle q (expressed in degrees).
- TranslateAll Dx Dy Dz
  Translate the position of all previously defined quadrics by (Dx, Dy, Dz).
- RotateAll x0 y0 z0 ux uy uz q
  Rotate all previously defined quadrics around the axis passing through the point (x0 , y0 , z0 ) and directed as (ux , uy , uz) by an angle q (expressed in degrees).
- End
  End of file.

### The three-dimensional object geometric description file
A solid object is defined as a solid shape delimited by a set of quadric surfaces that separates the space inside from the space outside it. The quadrics delimiting an object must be properly oriented, in such a way that their normal vectors are directed outward with respect to the object itself.
- Only convex objects are allowed in XRMC. Non-convex shapes can be built by combining convex objects. The demo files show some examples of how to build non-convex shapes.
- The surfaces delimiting different objects can not be in contact with each other. The users have to pay particular attention to this point, because the code does not make any check on it. If the user wants two objects to be in contact with each other (for instance when building non-convex shapes by joining convex objects) a workaround is to separate them using two different quadrics, very close to each other but separated by a small gap, in such a way that the effect of the intermediate space on the radiation is negligible. The demo files show some examples of this trick.
- An object may contain other objects, or it may be contained in another object, as far as their delimiting surfaces are not in contact.
All objects must be contained in a finite region of space, called sample region.

geom3d device file header:

Newdevice geom3d	; Device type
name (string)	; Device name

Commands:

QArrName name
name (string): quadricarray input device name;

CompName name
name (string): composition input device name;

Object name
name (string): 3d object name; defines a new object;
phase-in-name
name of the phase (material) inside the object;
phase-out-name
name of the phase (material) surrounding the object;
Nq
number of quadrics that define the object surface;
quadric-name-1 quadric-name-2 ….. quadric-name-Nq
names of the quadrics that define the object surface;

End
End of file.
### The sample file
When a photon exits from the source or when it is produced by a scattering/fluorescence emission process, its trajectory is characterized by its position vector rph and by its direction vector uph. The program evaluates the intersection of this trajectory with the quadric surfaces delimiting the objects, and divide it in Ns steps with uniform phases. Each step is a segment of the trajectory delimited by its intersection with different objects. There are two possible modalities of extracting the next interaction position:
1. extract the interaction position according to the interaction probability distribution along the trajectory, which is evaluated from the linear absorption coefficient of the phases and from the steplengths of the paths;
2. extract a step at random using a random integer number 0≤m<Ns , Extract a random position on step m using a uniform probability distribution, and multiply the weight associated to the event by a proper factor;
The first modality is that of the traditional Monte Carlo approach. The second one is sometimes used for variance reduction. It can be useful, for instance, when an object that emits a relevant fluorescence signal is surrounded by a strongly absorbing material, so that the probability that the incident radiation reaches such object is relatively low.

sample device file header:

Newdevice sample	; Device type
name (string)	; Device name

Commands:

SourceName name
name (string): source input device name;

Geom3DName name
name (string): geom3d input device name;

CompName name
name (string): composition input device name;

WeightedStepLength val
modality that will be used for the extraction of the next interaction position:
val = 0: method 1) described above;
val = 1: method 2) described above;

FluorFlag val
activate Fluorescence (0/1); it can be useful to deactivate it in imaging experiments	where fluorescent emission is not relevant, to save computational time;

ScattOrderNum NI
NI (integer): maximum scattering order (0: transmission, 1: first order scattering or	fluorescence emission, 2: second order scattering or fluorescence emission, …)
M1
multiplicity of simulated events for order 0;
   …..
MNI
multiplicity of simulated events for order NI ;

End
End of file.

As discussed previously, the total number of generated events is given by the product of the multiplicities in the spectrum, in the interactions with the sample and in the detector pixels.
### The output file
By default, the output file is saved in raw binary format. The detector bin contents are written in C double format (64 bit real). If you prefer to save the data in ascii format, you can use the AsciiFlag command, which is described in the detectorarray file section.
The total number of entries is:
N. of scattering orders × N. of columns × N. of rows × N. of energy bins
with the energy bins running faster.
If the header flag is set to 1 in the detector file, then the bin contents are preceded by a 60-bytes-long header, also in binary format, containing the following information:
- N. of scattering orders (C int format, 32 bit integer)
- N. of columns (C int format, 32 bit integer)
- N. of rows (C int format, 32 bit integer)
- Pixel size Sx (C double format, 64 bit real)
- Pixel size Sy (C double format, 64 bit real)
- Exposure time in sec. (C double format, 64 bit real)
- Pixel content type (C int format, 32 bit integer)
- N. of energy bins (C int format, 32 bit integer)
- Minimum bin energy (C double format, 64 bit real)
- Maximum bin energy (C double format, 64 bit real)

## Description of the C++ classes
In this section we will cover all of the C++ classes that are defined in XRMC, and that can be extended by the users in order to create custom devices.

### Vector and matrix operations
Many of the calculations made by the program involve operations on three-dimensional vectors and on 3 × 3 or 4 × 4 real matrices. For such reason, three specialized classes, vect3, matr3 and matr4 have been implemented. Those classes exploit the operator overloading feature of the C++ programming language in order to represent vector and matrix operations in a natural and readable manner. For instance,
a change of coordinates from the local coordinate system associated to a device to the absolute coordinate system of XRMC can be expressed by the vector operation:
r=r0 +ui ·x+uj ·y+uk ·z

with r the the position vector of a point relative to the absolute coordinate system, r0 the position vector of the local coordinate system origin, ui , uj and uk the direction vectors of the local coordinate system axis and x, y and z the coordinates of the point relative to the local coordinate system. This operation can be expressed using the vect3 class as:
r = r0 + ui · x + uj · y + uk · z

with r, ui, uj and uk objects of the class vect3, x, y and z are of the C/C++ type double, and ``+'' and ``*'' are overloaded operators of the vect3 class.
An alternative approach was based on more general matrix and vector base classes, and derived classes for specific dimensions. However, the computation time over- head of this approach was relevant, therefore the final choice was to use specialized classes for three and four dimensions.
The vect3 class member variables are the three vector components, while its main member functions are:
- product/division of a vector by a scalar;
- sum and difference between vectors;
- scalar product of two vectors;
- vector product;
- modulus;
- vector normalization;
The first three are represented by the C/C++ algebraic operators, while the vector product is represented by the symbol ``ˆ''.
The matr3/matr4 member variables are the 9/16 matrix elements, while their main member functions are:
- matrix multiplication;
- matrix transposition operator;
- multiplication of a matrix by a vector;
- rotation matrix of an angle θ around an axis with direction u;
### The photon class
XRMC uses a specialized photon class to describe x-ray photon transport and interaction with matter. A local coordinate system is associated with the photon, with the direction of the three axes x, y, and z defined by three unit vectors iph, jph, kph , with kph the photon direction, iph the polarization vector, which is always perpendicular to the photon direction, and jph, the unit vector perpendicular to both iph and kph. The other variables that describe the photon state are its energy E and its weight w.
The main member variables of the photon class are:
- double w: event weight;
- double E: photon energy;
- vect3 x: photon position vector;
- vect3 ui, uj, uk: direction vectors of the photon local coordinate system;
The main member functions of the photon class are:
- int MoveForward(double step_length): moves the photon in the direction uk by a distance step_length;
- int ChangeDirection(double theta, double phi): updates the photon direction using the polar angle theta and the azimuthal angle phi in the local coordinate system;
- int MonteCarloStep(sample *Sample, int *iZ, int *iType): evaluates the photon next interaction atomic number, type and position;
- int CSInteractions(int Z, double *mu_interaction, double *cs_tot): evaluates the cross sections of the three interaction types with the extracted element;
- int InteractionType(double *cs_interaction, double cs_tot): extracts the interaction type (elastic/inelastic scattering or fluorescence);
- int SetFluorescenceEnergy(int Z): set the photon energy to that of the fluorescent emission line;
- intScatter(int Z,int interaction_type); checks the interaction type and launches the corresponding method;
- int Scatter(int Z, int interaction_type, vect3 v_r): analogous to the previous function, but with the photon forced to have the direction v_r;
- int Fluorescence(): generates a fluorescent emission process;
- int Coherent(int Z): generates an elastic scattering process;
- int Incoherent(int Z): generates an inelastic scattering process.
### The device and bodydevice classes
In XRMC the term device refers to a C++ object that is created in order to be used by the simulation, and whose parameters are loaded from the corresponding file. It does not necessarily correspond to a physical device. For instance, the phase (material) array and the sample are considered to be devices. The term device is also the name of the abstract base class from which all concrete device classes are derived. The member variables of the device class are:
- the device name;
- the device type;
- an index for the loop on the events;
The main virtual methods of the class are:
- the ImportDevice method, used to connect a device to one or more input devices through a device map;
- the Load method, used to load the device parameters from an input file;
- the SetDefault method, which sets default values for device parameters;
- the Begin, Next and End methods, used to control the loop on the events;
- the Run method;
- the Save method, which saves the device output to a file;
The last two methods are not used by all devices. Only the detectorarray device has implemented them, in the current version of the package.
Another important abstract class used in XRMC, derived from the device class, is the bodydevice class. Besides the device member variables and functions, a bodydevice is characterized by a position and a local coordinate system, through the following member variables:
- vect3 X: bodydevice position;
- vect3 ui, uj, uk: local coordinate system axis directions.
The classes derived from the bodydevice class are the basesource and detectorarray classes. The basesource class is an abstract class for x-ray sources. It is the base class for all classes that can send x-ray photons to other devices, which in the current version of the code are the source class (which can send photons to the sample or to the detector devices) and the sample class (which can send photons to another sample or to a detector devices). In future releases of the program, other classes derived from the basesource class could be used to represent optical elements, such as x-ray mirrors, multilayers and x-ray lenses.
The methods of the basesource class are:
- the ModeNum method, used to specify the number of modes the device can work as. With regard to the sample derived class, it refers to the number of scattering orders used in the simulation;
- the Out_Photon method, used to send a photon to the output device;
- the Out_Photon_x1 method, used to generate an event with a photon forced
  to be directed toward the position x1, specified by the output device;
On the other hand, the concrete classes that are directly derived from the abstract device class are the composition, spectrum, and geom3d classes.
Each device can be connected to one or more input devices. The following figure shows schematically how the concrete devices used in a standard setup are interconnected. The classes of those devices are described in the following sections.

Figure 2. C++ classes associated to the main XRMC devices and connections used in a standard setup.

### The source class
The current version of the code assumes that the x-ray beam is produced by a point source or by an extended source with a three-dimensional Gaussian distribution. A local coordinate system is attached to the source, which is determined by the vector position of the origin rs and by the orthonormal unit vectors is , js and ks , which correspond to the directions of the local x , y , and z axis, respectively. The local z axis represents the main source direction, while the local x and y axes are used to define the beam polarization and angular aperture. Let θs and φs be the polar and azimuthal angle, respectively, relative to the source coordinate system. The user can specify the angular apertures θx and θy in the x and in the y direction, respectively. In general, the angular aperture of the source is elliptical and it is defined by the inequality:

The source intensity distribution is assumed to be uniform within the solid angle delimited by this angular aperture.
The main member variables specific of the source class (not belonging to its base classes) are the following:
- spectrum *Spectrum: pointer to the input spectrum device;
- string SpectrumName: name of input spectrum device;
- double Thx, Thy: beam divergence (θx and θy);
- double Omega: source aperture solid angle;
- double Sigmax, Sigmay, Sigmaz: source size in the local coordinate system.
The main member functions specific of the source class are:
- double CosThL(double phi); maximum value of the polar angle θ for a specified value of φ;
- intPhotonDirection(photon* Photon, int pol):extract the initial direction and polarization of a photon;
- int SetPhotonAxes(photon *Photon, int pol): build the photon local axis based on its direction and polarization;
- double POmega(vect3 vr): probability per unit solid angle that a photon has direction vr .

### The spectrum class
The energy spectrum is modeled as the sum of two components: a set of discrete lines and a continuous component. The radiation can be unpolarized, partially polarized or completely polarized. The lines can have a Gaussian or a Dirac δ distribution (the latter one being simply a particular case of Gaussian distribution with σ = 0). Each line is specified by its mean energy, its intensity (two components if polarized), and its standard deviation.
The continuous component is defined by N samples at different energies and the corresponding height of the spectral distribution.
The main member variables of the spectrum class are the following:
- int PolarizedFlag: flag for polarized(1) / unpolarized(0) beam;
- int LoopFlag: flag for loop on all lines and all intervals of the spectrum;
- int RandomEneFlag: flag for extracting random energies in the intervals;
- int ResampleFlag: flag for resampling the continuous spectrum;
- int EneContinuousNum: number of sampling points in the continuous spectrum;
- double *ContinuousEne: energies of sampling points;
- double *ContSIntensity[2]: intensity at sampling points for the two polarization components;
- double ContinuousEnergyRange: energy range of the continuous spectrum;
- double ContinuousIntensity: total continuous intensity;
- double MaxIntensity: maximum continuous intensity;
- double *IntervalIntensity[2]: intensities of the intervals for the two polarization components;
- double *IntervalWeight[2]: weights of the intervals for the two polarization components;
- double *IntervalCumul: cumulative distribution of the intervals;
- int EneLineNum: number of discrete lines of the spectrum;
- double *LineEne: energies of the discrete lines;
- double *LineSigma: widths (sigma) of the discrete lines;
- double *LineIntensity[2]: intensities of the discrete lines for the two polarization components;
- double DiscreteIntensity: total intensity of the discrete spectrum;
- double *LineWeight[2]: weights of the discrete lines for the two polarization components;
- double *LineCumul: cumulative distribution of the lines;
- int ResampleNum: number of resampling points of the continuous spectrum;
- double Emin, Emax: minimum and maximum resampling energy;
- int ContinuousPhotonNum: number of events to be extracted for each interval;
- int ContinuousPhotonIdx: index of the event extracted for the interval;
- int LinePhotonNum: number of the events to be extracted for each discrete line;
- int LinePhotonIdx: index of the event extracted for the line;
- int PolIdx: index of polarization type (0: x, 1: y);
- int ModeIdx: mode index: continuous spectrum (0) or discrete lines(1);
- int IntervalIdx: index of the interval of the continuous spectrum;
- int LineIdx: index of the discrete line;
- double TotalIntensity: total intensity;
The main member functions specific for the spectrum class are the following:
- int ExtractEnergy(double *weight, double *Energy, int *polarization): generates a random energy value and polarization type;
- int ContinuousRandomEnergy(double *Energy, int *polarization): generates a random energy value from the continuous spectrum;
- intExtractSpectrum(double trial_energy, double*x_intensity, double*y_intensity): returns the intensity of the continuous spectrum at the given energy value;
- int DiscreteRandomEnergy(double *Energy, int *polarization): generates a random energy value from the discrete part of the spectrum;
- int IntervalRandomEnergy(double *E, int interval_idx, int pol_idx): extract the energy value and polarization type from a specified interval of the continuous spectrum distribution;
- int Resample(): method for resampling the continuous spectrum.

### The phase class
The sample is composed of a number of materials called phases. Each phase is assumed to be homogeneous. Each phase is characterized by the number of atomic species that define it, through a list of the atomic numbers and weight fractions of these species, and by its mass density;
The main member variables of the phase class are:
- int Nelem: number of elements in the phase;
- double Rho: mass density of the phase in g/cm3;
- int *Z: atomic number array;
- double *W: weight fraction array;
- double *MuAtom: atomic interactions total cross section array;
- double LastMu: linear absorption coefficient calculated at the current energy.
The main member functions are:
- int Mu(double E): evaluates the absorption coefficient at energy E;
- int AtomType(int *Z, double *mu_atom): extract the atomic species with which the interaction will occur;

### The composition class
The composition class contains an array of the phases used by the simulation. Its main member variables are:
- int Nphases: number of phases;
- int MaxNPhases: maximum number of phases;
- phase *Ph: phase array;
- phase_map PhaseMap: map of phases with their names.
The main member function specific of this class is:
int Mu(double E): evaluates the absorption coefficient of each phase.

### The quadric class
The sample geometry is described through a set of quadric surfaces, which are used to define the surfaces of solid objects. A quadric is a surface in the three- dimensional space defined as the locus of zeros of a quadratic polynomial.
The main member functions of the quadric class are:
- matr4 Matr: 4 × 4 real matrix;
- int Ninters: number of intersection of a trajectory with the quadric;
- double tInters[2]: parametric coordinates of the intersections;
- int Enter[2]: crossing directions: from outside to inside or viceversa.
The main member functions of the quadric class are:
- double Prod3(double *x, double *y): evaluates the quadratic form Aij xi yj on 3d vectors;
- double Prod4(double *x, double *y); evaluates the quadratic form Aijxiyj on 4d vectors;
- int Inside(vect3 x): checks if x is inside (0) or outside (1) the quadric;
- int Ellipsoid(double *x0, double *a): builds an ellipsoid quadric;
- int Plane(double *x0, double *u): builds a plane quadric;
- int CilinderX(double *x0, double *a): builds a cylinder parallel to the x axis;
- int CilinderY(double *x0, double *a): builds a cylinder parallel to the y axis;
- int CilinderZ(double *x0, double *a): builds a cylinder parallel to the z axis;
- int Intersect(vect3 x0, vect3 u): intersections of a line with the quadric;
- int Transform(matr4 M): congruence transform of the quadric with matrix M;
- int SetElem(int i, int j, double elem): sets Aij and Aji to the value elem.
### The quadricarray class
The quadricarray class contains an array of the quadrics used by the simulation. Its main member variables are:
- int Nquadr: number of quadrics in the array;
- quadric *Quadr: pointer to the quadric array;
- quadric_map QuadricMap: map of the quadrics with their names.
### The qvolume class
A solid object is defined as a solid shape demarcated by a set of quadric surfaces that separates the space inside from the space outside it. The quadrics limiting an object must be properly oriented, in such a way that their normal vectors are directed outward with respect to the object itself.
In the current version of the implementation, objects must be convex: the user is expected to take care of splitting non-convex objects into convex ones when using them in the simulation.
An object may contain other objects, or it may be contained into another object, as far as their limiting surfaces are not in contact.
The class used in XRMC to represent three-dimensional objects is called qvolume. The member variables of this class are:
- int Nquadr: number of quadrics delimiting the object;
- int iPhaseIn: index of the phase inside the object;
- int iPhaseOut: index of the phase surrounding the object;
- string PhaseInName: name of the phase inside the object;
- string PhaseOutName: name of the phase surrounding the object;
- quadric **Quadr: array of pointers to the quadrics delimiting the object.
Its main member function is:
int Intersect(vect3 x0, vect3 u, double *t, int *iph0, int *iph1, int *n_inters): method for finding the intersections of a line with the object.

### The geom3d class
The geom3d class contains an array of the three-dimensional objects used in the simulation.
Its main member variables are:
- quadricarray *Qarr: array of quadrics used in the geometric description;
- string QarrName : quadricarray input device name;
- composition *Comp: input composition device;
- string CompName: composition input device name;
- int NQVol: number of 3d objects used in the geometric description;
- int MaxNQVol: maximum number of 3d objects in the geometric description;
- qvolume *Qvol: array of 3d objects;
- string **QvolMap: map of the quadrics delimiting the objects.
The main method specific for the geom3d class is:
int Intersect(vect3 x0, vect3 u, double *t, int *iph0, int *iph1, int *n_inters): method for finding the intersections of a straight line with all quadrics demarcating the three-dimensional objects.
### The path class
When a photon leaves the source or when it was produced by a scattering or fluorescence emission process, it follows a straight trajectory defined by its position vector rph and by its direction vector uph. The program evaluates the intersection of this trajectory with the quadric surfaces demarcating the objects, and divides it into Ns steps with uniform phases. Each step is a segment of the trajectory delimited by its intersection with different objects. The path class holds information about the intersection of a trajectory with the quadrics and about the segments between consecutive intersections.
The main member variables of the path class are:
- int Nsteps: number of intersections of a trajectory with all the quadrics in the sample;
- double *t: array of the intersections (distances from the starting coordinate);
- double *Step: step lengths between consecutive intersections Si;
- int *iPh0: array of the entrance phase indexes;
- int *iPh1: array of the exit phase indexes;
- double *Mu: absorption coefficient at each step μi;
- double MuL: sum of μi × Si;
- double *SumMuS: cumulative sum of μi × Si.
The main member functions are:
- int StepMu(composition *comp): evaluates the absorption coefficient at each step of the intersection;
- double StepLength(int *step_idx, double *weight): extracts the next interaction position using the standard MC approach;
- double WeightedStepLength(int *step_idx, double *weight): extract the next interaction position using the weighted steplength approach.

### The sample class
The sample class is a container used to join the information about the sample composition, the geometrical description and the type of interactions that can occur in the sample. The main member variables of this class are:
- basesource *Source: input source device;
- string SourceName: input source name;
- geom3d *Geom3D: input geom3d device;
- string Geom3DName: input geom3d name;
- composition *Comp: input composition device;
- string CompName: input composition device name.
- path *Path: object storing all info about intersections;
- int ScattOrderNum: number of scattering orders;
- int *PhotonNum: event multiplicity for each scattering order;
- int ScattOrderIdx: scattering order index;
- int PhotonIdx: event index.
The main member functions specific of the sample class are:
- int Intersect(vect3 x0,vect3 u); evaluates intersection of a trajectory with the sample objects;
- double LinearAbsorption(vect3 x0, vect3 u): evaluates the absorption coefficient at each step of the intersections;
- int Out_Photon_x1(photon *Photon, vect3 x1): generates an event with a photon forced to end on the point x1.

### The detectorarray class
In general, the program can simulate two-dimensional array detectors with energy binning for each pixel. A single element detector can be simulated as a special case of array detector with only one pixel. The pixel shape can be defined as rectangular or elliptical. The latter possibility is particularly useful when a round, single element detector has to be simulated.
A local coordinate system is associated with the detector, specified by the vector position of its geometric center rd and by the orthonormal unit vectors id, jd and kd, which are the directions of the local x , y , and z axis, respectively. The local z axis is perpendicular to the detector surface, while the local x and y axes are parallel to the detector rows and columns, respectively.
Two acquisition methods are available:
1. fluence: each channel simply counts the number of photons that it detects;
2. energy fluence: each channel sums up the energy of the photons that it detects.
The energy response of the detector can eventually be taken into account through using the first method with a sufficient number of energy bins and if a proper post- processing of the acquisition is performed.
The main member variables of the detectorarray class are:
- basesource *Source: input device (typically the sample device);
- string SourceName: name of the input device;
- int NX, NY, N: number of rows (NY), columns (NX) and pixels (NX×NY);
- double PixelSizeX, PixelSizeY, PixelSurf: pixel size and surface (cm2) ;
- int Shape: pixel shape (0: rectangular, 1: elliptical);
- vect3 *PixelX: pixel coordinates array;
- double *Image: acquired image array;
- double ExpTime: exposure time (seconds);
- int PhotonNum: multiplicity of simulated events per detector pixel;
- int Nbins: number of energy bins;
- int PixelType: pixel content type: 0: fluence, 1: energy fluence, 2: fluence with energy binning, 3: energy fluence with energy binning;
- int SaturateEmin: flag to saturate energies lower than Emin;
- int SaturateEmax: flag to saturate energies greater than Emax;
- double Emin, Emax: minimum and maximum bin energy
The main member functions are:
- int Acquisition(): run the acquisition;
- int Clear(): clear the detector pixel bin contents;

## Examples
The examples can be found in the subdirectories of xrmc/examples. The examples are described by comments in the corresponding input files. To run an example, go to the corresponding subdirectory and type the command:
xrmc input.dat
At the end of the simulation, the output will be stored in the file image.dat (or output.dat for the fluor_layers example). The output of the examples 1-6 are images in raw binary format, which can be opened with any image visualization program able to import such format. For instance, the figures in this document have been produced using ImageJ, which is a public domain image processing program, freely available for several platforms. In case you want to open the output images of the examples using this program, select from the menu:
file → import → raw...
chose the image and use the following settings in the import form:
- Image type: 64-bit real;
- Width: N. of columns;
- Height: N. of rows;
- Offset to first image: 60 if the image contains the header, 0 otherwise;
- Number of images: N. of scattering orders (1 if only transmission was simulated);
- Little endian byte order: depends on the architecture of your system;
Example 7 represents the simulation of a x-ray fluorescence spectroscopy experiment. A simple program is provided with this example, in the same directory, to simulate a Silicon Drift detector response.

### Cylindrical shell
Example 1: simulating a cylindrical shell using convex objects, directory cylind_shell.
To simulate a cylindrical shell using only convex objects, two objects have been used:
- An external full cylinder, delimited by two planes;
- An internal empty cylinder (the phase inside it is vacuum, phase index=0), delimited by other two planes very close to those of the external cylinder but separated from them by a small gap
Figure 2 shows the output image. Image size: 400 × 400

Figure 2 Example of simulation of radiographic images of a cylindrical shell This example is described by comments in the corresponding input files.

Figure 3 Schematic representations of two ways of building a star shape by combining convex objects. In the quadric definition files, the planes between adjacent objects are separated by a very small gap, however in this figure their separation is increased for clarity. (a) Geometrical objects used to compose the star shape described in example 2. (b) Planes used to define the geometrical object surfaces described in example 2. (c) Geometrical objects used to compose the star shape described in example 3. (d) Planes used to define the geometrical object surfaces described in example 3. All objects are delimited by two planes parallel to the figure plane. Those examples are described by comments in the corresponding input files.

### Star shape 1
Example 2: one way of building a star shape by combining convex objects, directory star1.
Figure 3(a) shows the geometrical objects used to compose the star shape. The five triangles are separated from the inner pentagon by small gaps. The phase inside the triangles and that inside pentagon are the same. Figure 3(b) shows the planes used to define the geometrical object surfaces. All objects are delimited by two planes parallel to the figure plane.
Figure 4(a) shows the output image. Image size: 400 × 400

### Star shape 2
Example 3: another way of building a star shape by combining convex objects, directory star2.
Figure 3(c) shows the geometrical objects used to compose the star shape. The five triangles are empty (i.e. the phase inside them is vacuum, phase index=0), and they are separated from the external pentagon by small gaps. Figure 3(d) shows the planes used to define the geometrical object surfaces. All objects are delimited by two planes parallel to the figure plane.
### Different type of quadrics
Example 4: an image with different types of quadrics, directory quadrics.
Figure 4(b) shows the output image. Image size: 400 × 400
### A wheel shape
Example 5: a wheel, directory wheel.
A wheel is built by combining different cylinders and using the rotation commands.
Figure 4(c) shows the output image. Image size: 400 × 400
### Objects with different compositions
Example 6: cylinders with different compositions, directory materials.
Four cylinders having different compositions (polymethyl methacrylate, adipose tissue, water, bone-equivalent plastic) and placed inside a polymethyl-methacrylate frame are simulated.
Figure 4(d) shows the output image. Image size: 400 × 400

        (a)	(b)

        (c)	(d)

Figure 4 Example of simulation of radiographic images of different shapes: a star shape (a), a thin spherical shell containing different types of quadrics (b), a wheel (c) and four cylinders having different compositions and placed inside a frame (d). All the examples are described by comments in the corresponding input files.

### X-ray fluorescence spectroscopy example
Example 7: x-ray fluorescence spectroscopy example, directory fluor_layers. Fig. 5 represents schematically the experimental setup. The source is an Ag-anode x-ray tube set to 40 kVp and  A current. The source spectrum is polychromatic and it was measured experimentally. The beam was collimated through a 1 mm wide cylindrical collimator. The detector is a 25 mm2 diameter Silicon drift detector (X-123SDD by Amptek) 500 mm thick. The sample is a parallelepiped made of the following three layers (ordered starting from the one closest to the source):
- a 200 m thick mixture layer incrustation simulation;
- a 300 m thick copper layer;
- a 2.5 mm thick mixture layer, similar to the first one.
The current version of XRMC does not include the simulation of the response of real detectors. The users must take care of this point by post-processing of the simulation output. For the example just described, a separate program is provided to simulate the response of a Silicon drift detector. This program can be found in the directory example/fluor_layers/src, A README file explains how to compile and run it. Figure 6 shows a comparison between the measured signal and the simulated one.

  Figure 5 Schematic representation of the experimental setup for the fluorescence spectroscopy example.

Figure 6 Comparison between simulated and measured signal for the fluorescence example.